Planning & Engineering Services Section

DATE:09-07-2015

A310-322:ST-AST (A/C SPECIFICATIONS )

| Aircraft type | : | A310-322 |
| --- | --- | --- |
| Registration | : | ST--AST |
| A/C serial No. | : | 437. |
| Date of manufacture | : | 1987. |
| Max take off weight | : | 153,000 KG. |
| Fuel capacity | : | 48872 USG. |
| Zero fuel weight | : | 113,000 KG. |
| No. Of Galleys | : | Four |
| Seating configuration | : | 12F / 229Y |
| A/C total hours | : | 61714 Hrs. |
| A/C total cycles | : | 16177 Cycles. |
| [C] check every | : | 15 MONTHS. |
| LAST [C] CHECK | : | 09-05-2006 |
| LAST STRUCTURE INSPECTION | : | 5YEAR CHECK JUL.02 |
| Next due check | : | MAJOR CHK (8C) |

engines

| item | engine No. 1 | engine no. 2 |
| --- | --- | --- |
| Engine type | JT9D-7R4E1 | JT9D-7R4E1 |
| S/N | P715837 | P715818 |
| TOTAL TIME | 27181 | 23621 |
| TOTAL CYCLE | 19356 | 9602 |
| T.T since last shop visit | 1962 | 2683 |
| T.C since last shop visit | 1007 | 1296 |
| T.T SINCE LAST O/H | 5450 | 2683 |
| T.C SINCE LAST O/H | 2127 | 1296 |
| Apu Missing |  |  |

LANDING GEAR :

| TYPE | LEFT MLG | R MLG | NLG |
| --- | --- | --- | --- |
| P/N | D22121300-15A | D22122300-15A | C23137010-12 |
| S/N | B219 | B220 | L375 |
| LAST O/H APP. O/H INTERVAL | 17/01/2004 08 YEARS/16000 CYC | 17/01/2004 08 YEARS/16000CYC | 17/01/2004 08 YEARS/12000CYC |
| CURENT L/G T.C. | 2939 CYC | 2939 CYC | 2939 CYC |
| REMAINING CYC. | 13061 | 13061 | 9061 |
| nEXT DUE O/H | JAN 2012 | JAN 2012 | JAN 2012 |

CARGO COMPARTMENT

| TYPE | fwd | AFT | BULK |
| --- | --- | --- | --- |
| DIMENSIONS (CM.) | (7.63 x 4.18 x 1.71) m (300.4x164.7x67.5) in | (5.070 x 4.170 1.670)m (199.5x164.3 x 65.9)in |  |
| USABLE VOLUME (CU | 50.3 m3 1780 cu.ft | 34.5 m3 1218 cu.ft | 17.3 m3 (611 cu.ft.) |

| TYPE | fwd | AFT | BULK |
| --- | --- | --- | --- |
| DIMENSIONS (CM.) | 1100 x 940 mm) (43x37 in.) | 2739 x 2385 mm (108x94 in.) | 1848 x 2400 mm (72 x 94.5 in). |

CARGO DOOR

Maintenance schedule according to SD operation specification as follows:

| CHECK | OPERATOR NOMENCLATURE | CALENDER |
| --- | --- | --- |
| Weekly | WEEKLY CHECK | 7 DAYS |
| 1A | 1-A CHECK | 400 FH |
| 2A | 2-A CHECK | 800 FH |
| 3A | 3-A CHECK | 1200 FH |
| 4A | 4-A CHECK | 1600 FH |
| “C” | 1-C CHECK | 15 MONTHS |
| 2C | 2-C CHECK | 30 MONTHS |
| 3C | 3-C CHECK | 45 MONTHS |
| 4C | 4-C CHECK | 60 MONTHS |
| 6C | 6-C CHECK | 90 MONTHS |
| 8C | 8-C CHECK | 120 MONTHS |

Major Avionics: ST-AST

| Description | Qty | MODEL OR P/N | Manufacture |
| --- | --- | --- | --- |
| TCAS ( TCAS II CHANGE 7 ) | 1 | 066-50000-2120 | BENDEX/KING |
| hf comm | 2 | 622-5272-001 | Collins |
| vhf comm | 2 | 822-1044-003 | Collins/ALLIED SIGNAL |
| selcal decoder | 1 | SC 2253A-MOD. F | TEAM |
| cockpit voice recorder | 1 | 93-A100-82 | FAIRCHILD |
| PRAM TAPE REPRODUCER | 1 | 980-0000-001 | SUNSTRAND |
| DDRMI | 2 | 622-5818-001 | COLLINS |
| atc transponder mode s | 2 | 066-01127-1101 | BENDEX/KING |
| dme interrogator | 2 | 622-4540-001 | COLLINS |
| RADIO ALTMETER | 2 | 9599-607-14901 | TRT |
| ADF RECIVER | 2 | 622-5222-002 | COLLINS |
| VOR/MARKER BEACON RECEIVER ( fm immunity ) | 2 | 822-0726-020 | COLLINS |
| ils RECEIVER ( fm immunity ) | 2 | 822-0282-002 | COLLINS |
| weather radar transcever | 2 | 20412170416 | BENDEX/KING |
| E. G. P.W. S | 1 | 965-0976-003-216-216 | SUNSTRAND |
| INERTIAL reference SYSTEM | 3 | 461800-0300-2201 | LITTON |
| DIGITAL FLIGHT DATA RECORDER | 1 | 980-4700-003 | SUNSTRAND |
| FLIGHT MANAGEMENT SYSTEM | 2 | 40552-10 | SMITH |
| FLIGHT WARNING COMPUTER | 2 | 35-0B5-3004-308 | Aerospatiale |

E.Bakri Hassan Ali

Planning & Engineering Services Mgr